## Slide 1: HESSI Spectrometer Thermal Analysis
Critical Design Review
UCB Thermal Engineering
2024-02-10

## Slide 2: Thermal Design Overview
Radiative and conductive heat transfer between Cryostat, spacecraft, and space
Design meets thermal constraints in Section 3.3
Primary dissipation via large bottom radiator surface
Conductive coupling through aluminum mounting flanges

## Slide 3: Thermal Requirements
Bus Side Interface: -10°C to +40°C
Spectrometer Side Interface: -20°C to +30°C
Detector Operating: -198°C to -190°C
Cryocooler Reject: < +50°C

## Slide 4: Thermal Model Results
Worst Case Hot: All interfaces within limits with 5°C margin
Worst Case Cold: Heaters maintain survival with 15W allocation
Transient Eclipse: Detector temp stable within 2°C

## Slide 5: Heater Design
4 independent programmable thermostats
Maximum 15W per channel
PID control with flight-adjustable gains
Platinum RTD sensors (100 ohm at 0°C)

## Slide 6: Spectrometer Power Dissipation
Science Mode: 88.5W total
Eclipse Mode: 17.5W (heaters + standby)
Dissipation primarily through bottom radiator
Conducted path: 2W maximum via mounting flanges

## Slide 7: Summary & Next Steps
Questions?